## Slide 1: CMP330: Allowing new Transmission Connected parties to build Connection Assets greater than 2km in length

## Slide 2: Allowing new Transmission Connected parties to build Connection Assets greater than 2km in length - Defect
Defect Identified:
CUSC definition of connection assets set down in 14.2.6:
14.2.6 Connection assets are defined as all those single user assets which:
a) for Double Busbar type connections, are those single user assets connecting the User’s assets and the first transmission licensee owned substation, up to and including the Double Busbar Bay;
b) for teed or mesh connections, are those single user assets from the User’s assets up to, but not including, the HV disconnector or the equivalent point of isolation;
c) for cable and overhead lines at a transmission voltage, are those single user connection circuits connected at a transmission voltage equal to or less than 2km in length that are not potentially shareable.
Part c) prevents a third party from constructing cable and overhead lines at transmission voltages that are over 2km
The 2km constraint can lead to more expensive connections and a longer connection time

## Slide 3: Allowing new Transmission Connected parties to build Connection Assets greater than 2km in length – Proposed Solution
Proposed solution:
To amend the definition of connection assets as follows:
14.2.6 Connection assets are defined as all those single user assets which:
a) for Double Busbar type connections, are those single user assets connecting the User’s assets and the first transmission licensee owned substation, up to and including the Double Busbar Bay;
b) for teed or mesh connections, are those single user assets from the User’s assets up to, but not including, the HV disconnector or the equivalent point of isolation;
c) for cable and overhead lines at a transmission voltage, are those single user connection circuits connected at a transmission voltage equal to or less than 2km in length that which are not potentially shareable and:
(i) equal to or less than 2km in length, unless
(ii) the relevant Transmission Owner, The Company and the User all agree that this limit should be revised, and that the asset specified should be defined as a Connection asset. Such agreement should not be unreasonably withheld.

## Slide 4: Allowing new Transmission Connected parties to build Connection Assets greater than 2km in length – Impact
Impact:
This mod introduces more contestability into the construction of connection assets.
The impact is more efficient connections which are potentially completed more quickly and/or at potentially lower cost
  The proposer has identified that they can construct a cable to connect their windfarm that will enable energisation four years earlier than if the asset is constructed by the transmission owner.
  The proposer also highlights that the asset they would like to construct is at 132kV and would be considered as contestable in England & Wales as a non-transmission voltage. However, they are unable to undertake this work in Scotland
  Intent is for the asset to be constructed by a third party then adopted by the transmission company
No direct impact on consumers or other generators. However, enabling transmission connected generation to connect more quickly and cheaply should benefit GB as a whole.