## Slide 1
ESO latest thinking on Expansion Constant wider review
Grahame Neale

## Slide 2: Reinforcement types
Broadly, all works on the transmission system achieve one or more of the following;
Increase network capacity
Increase utilisation of existing capacity
Extend life of existing capacity
The current Expansion Constant only focuses on a subset of (1) (i.e. not all works have a km value such as substation works) and uses the following data from Transmission Owners;
The cost of construction per route km
The amount of route km’s installed over the last 10 years
Average asset life
Looking for industry thoughts on the following slides

## Slide 3: Current Ambition/Thoughts
Broadly, all works on the transmission system achieve one or more of the following;
Increase network capacity
Increase utilisation of existing capacity
Extend life of existing capacity
Looking to enhance the Expansion Constant to capture as many of the above work types as possible – if we can create a suitable methodology… Also looking to;
Revise 10 years of historic data to 5 years of historic and 5 years prospective
Keep the current frequency of updating the Expansion Constant (i.e. start of each price control and annual index-linked revisions within a price control)
Keep/review approach for assets that can be upgraded

## Slide 4: Challenges
To capture these other types works in the Expansion Constant, the following challenges need to be overcome;
Methodology – should the Expansion Constant account for the above works equally or be weighted in some way?
‘Zero values’ and proxies – Some works don’t provide all the variables needed unless secondary effects or proxies are considered. For example, substation works have no length unless circuits connected to that substation are considered
Data availability – Data to apply this retrospectively may not exist and so it may only be possible to apply to current/future works.
STCP 14-1 changes – Section 3.5 of STCP14.1 lists the data NGESO will receive from Transmission Owners. This will need to be considered in full alongside any CUSC changes.

## Slide 5: Next Steps
Still a lot of to do…
Keep engaging with industry via TCMF & bilaterally (Grahame.Neale@nationalgrideso.com)
Discussions with Transmission Owners to understand data possibilities
Understand linkages to CMP315 (may deliver part of this?)
Develop some options for methodologies
Write and raise CUSC/STC mods.
No change to timeline from Jan’s TCMF;
Raise modification in spring 21 for a decision in September 2022
April 2023 implementation

## Slide 6
Refresher on what CMP315 is seeking to achieve
Nick Sillito

## Slide 7: CMP315
Terms of Reference
Defect
The locational element of the Transmission Network Use of System (TNUoS) charge converts the “MWkm” figure calculated by the locational model and converts this figure into a locational cost (GBP/kW) for connecting generation and/or demand at a particular node. There are two potential issues with this process:
Not all assets used by the transmission system are included in the calculation of the MWkm figure (for example 400/275 kV transformers are excluded); and
ii. The expansion constant (used to convert MWkm to GBP/kW) assumes that the life and capacity of and asset can be fully flexed to meet a connectee’s requirements (for example if a customer required 300 MW of capacity over 25 years, the TO may – as the most cost-effective solution – construct a 500 MW asset with a life of 55 years). Therefore, the connectee would only be charged a proportion of the costs actually incurred by the TO (the balance of the cost would be recovered through the residual)

## Slide 8
Discussion as to how CMP315 fits in with wider Expansion Constant Review All

## Slide 9: CMP315 and new Modification – Governance Rules to be aware of
CMP315 is a “Pending CUSC Modification Proposal” and under 8.16.6 any new Modification Proposal (unless Directed by Authority) will be rejected by the Panel if it has “substantially the same effect” as CMP315
The new Modification Proposal can be amalgamated with CMP315 as per 8.19.2 and 8.19.3 if defect the same.
CMP315 could also be withdrawn by the Proposer under 8.16.10 and the scope of CMP315 included within the ESO’s wider Expansion Constant Modification - need to ensure that withdrawal notification timescales have elapsed for CMP315 before the New Expansion Constant Modification is presented to Panel