## Slide 1: Telephony for Virtual Control Points Mark Bingham BEng CEng FIET National Grid IT 21 December 2021

## Slide 2: Overview
An increasing number of BM Participants are adopting modern technology for voice communications with ESO
This often involves establishing a virtual Control Point using geographically dispersed personnel
Traditional Control Telephony solutions are not suitable for this way of working
The following slides show the options available for Telephony between ESO and various Control Point locations

## Slide 3: Control Telephony: Control Point local to Substation
Connectivity
via NGET OpTel fibre network
Solution meets 72hrs power back-up requirement

## Slide 4: Control Telephony: Control Point local to Substation
Connectivity
via NGET OpTel fibre network & Scottish TO OpTel network
Solution meets 72hrs power back-up requirement

## Slide 5: Control Point up to 70km from Substation
Leased Openreach fibre circuit to Control Point e.g. Optical Spectrum Access (OSA)
GB Coverage with support from Scottish TOs
Not suitable for overseas Control Points
Telephony Solution meets 72hrs power back-up requirement
BM Participant must procure compliant network

## Slide 6: Control Telephony: Remote Control Point
Connectivity via Leased MPLS service to Control Point
Reasonable endeavours that power resilient nodes will be selected for Leased MPLS service by Comms Provider in order to meet 72hrs power back-up requirement.
But not guaranteed
BM Participant must procure compliant network

## Slide 7: Control Telephony: Remote Control Point
Connectivity via Leased MPLS service to Participant Data Centre
Reasonable endeavours that power resilient nodes will be selected for Leased MPLS service by Comms Provider in order to meet 72hrs power back-up requirement.
But not guaranteed
BM Participant must procure compliant network

## Slide 8: Remote Control Point
Public Telephony via SIP Trunks to Participant Data Centre
SIP carried over Comms Provider’s MPLS network but we have no control over use of power resilient nodes. Also, SIP could suffer from call congestion at peak times
BM Participant must procure compliant network

## Slide 9: Virtual Control Point
Data Centres and Control Points may be in different continents
Public Telephony via SIP Trunks to Participant Data Centres
SIP carried over Comms Provider’s MPLS network but we have no control over use of power resilient nodes. Also SIP could suffer from call congestion at peak times.
Higher risk of International Connections failing during times of power system stress
BM Participant must procure compliant network

## Slide 10: Virtual Control Point
Data Centres and Control Points may be in different continents
Leased MPLS
& private SIP Trunks to Participant Data Centres
Reasonable endeavours that power resilient nodes will be selected for Leased MPLS service by Comms Provider in order to meet 72hrs power back-up requirement.
But not guaranteed especially for International circuits
BM Participant must procure compliant network