## Slide 1: Reference Node CMP423
Workgroup 2
April 2024

## Slide 2
Actions
Proposer action 4 regarding: TOR 4 & 5
Other WG actions regarding: TOR 2, 3, 7

## Slide 4: Action 4: What does TOR 4 mean ?
“Consider the impact on tariffs that may arise from changes in the way circuits may be placed into either Peak Security and Year Round buckets” (TOR 4)
The change in reference node has no impact on which buckets the circuits are placed into.
The buckets are determined by the background flow before considering the incremental flows and reference node, therefore circuits will remain in the same buckets, regardless of the change in reference node.

## Slide 5: Action (TOR 2): Year Round connection map
“Consider implications for the network sharing calculation in the Transport and Tariff model” (TOR 2)
Transport and Tariff Model
Connection map used to calculate Year Round shared vs not-shared MWkm
Generation weighted reference node “zero point” likely to be a different location
Next steps:
Check where the baseline demand weighted average reference node currently is located ?
Where would the new Year Round generation weighted average reference node be located ?

## Slide 6: Action 4: What does TOR 5 mean ?
“Consider the impact on demand customers contribution from a different location signal especially those unable to react to those signals” (TOR 5)
Chart: £/kW HH Demand tariff
| Northern Scotland | Southern Scotland | Northern | North West | Yorkshire | N Wales & Mersey | East Midlands | Midlands | Eastern | South Wales | South East | London | Southern | South Western
2022/23 | 27.4467 | 35.4657 | 44.6819 | 51.4075 | 51.8394 | 53.4067 | 55.5285 | 57.1939 | 57.9535 | 58.462 | 60.1991 | 63.6878 | 62.2637 | 63.7477
2024/25 "unfloored" | -32.9251 | -24.3999 | -11.9964 | -4.7945 | -4.1902 | -2.7537 | -0.14704 | 2.3731 | 0.82537 | 4.5035 | 3.8592 | 5.7327 | 6.8697 | 8.1989
2024/25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.3731 | 0.82537 | 4.5035 | 3.8592 | 5.7327 | 6.8697 | 8.1989
Illustrative Reference Node "unfloored" | -20.9251 | -12.3999 | 0.003632 | 7.2055 | 7.8098 | 9.2463 | 11.853 | 14.3731 | 12.8254 | 16.5035 | 15.8592 | 17.7327 | 18.8697 | 20.1989
Illustrative Reference Node | 0 | 0 | 0.003632 | 7.2055 | 7.8098 | 9.2463 | 11.853 | 14.3731 | 12.8254 | 16.5035 | 15.8592 | 17.7327 | 18.8697 | 20.1989
Illustrative impact on demand charges
Before 2023/24, Triad charge much higher
From 2023/24 locational reduced floored at £zero
(TCR decision)
Gen Ref Node would improve demand signal
  Higher locational tariff
  Lower Residual tariff – Fixed charge per site
TNUoS Task Force - New demand modification
Split out Peak Security vs Year Round charges
Widen definition of Triad
Remove “floor at £zero”
Opportunity to change which customers pay
Next steps
ESO to provide actual tariff model impacts

## Slide 7: Action 6: Reflect on TOR 7
Proposed solution: different generation weighted scaling between Peak Security vs Year Round backgrounds
Peak Security background
Pro-rata generation based on scaled TEC including interconnectors and storage
Rationale is that, for the purpose of the Peak Security Background, interconnectors and storage can act as substitutes for firm generators regarding the provision of capacity.
Year Round background
Pro-rata generation based on scaled TEC, excluding interconnectors and storage
Rationale is that, for the purpose of the Year Round background, interconnectors and storage are not substitutes for generators regarding the provision of primary energy.
“Consider if the assumption that change in generation will displace generation elsewhere is an appropriate assumption now and in the future”

## Slide 8: Action 6: Reflect on TOR 7
Rationale for the assumption: In practice, generation scales to meet demand, demand does not scale to meet generation
Government sets targets for generation to meet demand, e.g. Contracts for Difference auction, Capacity Mechanism where:
  Generator winning a contract will tend to displace a different generator that did not win.
  If a generator closes, then more generation capacity needs to be procured through a future auction to replace it
Consistent with: reality of operating the energy system, ESO Network Options Assessment (NOA) process and the Security and Quality of Supply Standards (SQSS)
Generation charges: Generation weighted Reference Node is more cost reflective for generation charges
Impact of an increase in generation best reflected by a corresponding decrease in generation elsewhere:
  Reductions in existing generation can only take place in locations where there is already existing generation that can close.
  Any displaced hypothetical alternative new generation, would also be best reflected by a weighted average of existing generation, because alternative new generation would be more likely to be weighted towards locations where there is already generation, not weighted towards locations where there is already demand.
Impact of a reduction in generation best reflected by a corresponding increase in generation elsewhere:
  For the purpose of providing a risk weighted average, corresponding increases in generation should take place in locations where there is already generation. This is because additional generation is more likely to occur at places where there is already generation due to other limiting factors, such as: where there is access to gas grid, cooling, brown field sites, planning consents, wind resource, seabed availability. By contrast, it is not appropriate for corresponding increases in generation to be weighted towards areas dominated by demand, such as London city centre.
Demand charges: Generation weighted Reference Node is more cost reflective for demand
Demand investment/closure decisions tend to be open-ended and independent of each other, so:
Increased demand at one location: An increase in demand at a location does not tend to cause a corresponding closure of existing demand at a different location. More realistically, an increase in demand would cause an increased requirement for increased generation, so its impact would best be reflected by modelling a pro-rata increase in generation.
Reduced demand at one location: A reduction in demand at a location does not tend to cause a corresponding increase in other demand at other locations. More realistically, a reduction in demand would cause a reduced requirement for generation, so its impact would best be reflected by modelling a pro-rata reduction in generation.
“Consider if the assumption that change in generation will displace generation elsewhere is an appropriate assumption now and in the future”

## Slide 9: Action 5 (TOR 3): Generation Capacities Become More Northern Over Time (FES Leading The Way)
“Consider potential locations for new generation such as via the TEC Register, seabed leasing, or other planning sources” (TOR 3)
Demand split remains similar over time (only 2025 shown here)
In 2025, generation capacity is already weighted to northern regions (Scotland and North of England)
By 2035, generation capacities become increasingly weighted to the north.
Data estimated based on ETYS 2023 report, Leading the Way FES Scenario
Chart: Generation Capacity (excl storage & IC) vs Demand (MW)
| Scotland | North of England | North Wales & Midlands | East of England | South Wales & South England
Demand 2025 | 4200 | 9000 | 19000 | 3900 | 16000
Gen Capacity 2025 | 21000 | 25000 | 13500 | 10500 | 10000
Gen Capacity 2035 | 63200 | 41000 | 14000 | 16000 | 10500

## Slide 10: Action 5 (TOR 3): Southern Low Carbon Build Offsets Fossil Closures
Low carbon & renewables capacities increase significantly in Scotland and North of England.
For N.Wales & Midlands, and S.Wales & S.England, low carbon build is similar to reduction in fossil fuel capacity.
  Only a small overall increase in southern Capacity
Data estimated based on ETYS 2023 report, Leading the Way FES Scenario
“Consider potential locations for new generation such as via the TEC Register, seabed leasing, or other planning sources” (TOR 3)
Chart: Change in generation capacities between 2025-2035
| Scotland | North of England | North Wales & Midlands | East of England | South Wales & South England
Demand 2025 | 4200 | 9000 | 19000 | 3900 | 16000
Fossil Fuel Capacity (MW) | -800 | -6000 | -9000 | -3000 | -7500
Low carbon & Renewable Capacity (MW) | 43000 | 22000 | 9500 | 8500 | 8000